Theme III: Sustaining the Early Warning Dialogue

USING THE SATELLITE REMOTE SENSING TECHNOLOGY FOR                   EARTHQUAKE DISASTER EARLY WARNING

Mahmood Hosseini1, Yasamin O. Izadkhah2

1Associate Professor, Head of Lifeline Engineering Department, and Director of Structural Engineering Research Center, International Institute of Earthquake Engineering and Seismology (IIEES), P.O. Box 19395-3913, Tehran, Iran;

Tel: (98) 21 229 3634 Fax: (98) 21 229 9479, Email: hosseini@dena.iiees.ac.ir

2 Ph.D. Candidate, Disaster Management Centre, RMCS, Cranfield University, Shrivenham, Swindon SN6 8LA, UK, Tel: 0044 1793 785125, Fax: 0044 1793 785883,

Email: Y.O.Izadkhah@rmcs.cranfield.ac.uk

INTRODUCTION

Satellite Remote Sensing Technology (RST) has been used in many developing countries, including Iran for a few civil purposes, particularly meteorological forecasting.  However, although Iran and many other developing countries are located in earthquake prone regions, still there is slight development in the use of this technology for seismic warning purposes.  One of the main reasons behind this fact is the lack of knowledge in disaster management authorities with respect to RST.  The slowness and inaccuracy of this technology, the complexity of earthquake phenomenon and its sequences, and finally the low resolution of satellite Remote Sensing (RS) images, and their long repeat period are among the other factors that constrain the use of this technique in earthquake disaster reduction.  Nevertheless, the recent developments in RST and the potentials of this technology for serving the disaster mitigation activities support the thought of using it for early warning purposes. It should be noted that the early warning concept of earthquake is different from what is usually meant by it in other natural hazards.  In fact, instead of using the RST for predicting the time of an earthquake occurrence, which is actually impossible, this technology can be used for earthquake disaster early warning, by providing the disaster management authorities with the reliable information about the extent of damage to buildings and facilities in stricken areas.

In this study, the practicability and other relative scientific, technical, and economical issues of using satellite RST in developing countries for earthquake disaster early warning are discussed.  Special attention is paid to Iran as a sample of developing countries, which is located in a seismically active region of the world and has disastrous experience of several catastrophic earthquakes in recent decades.  At first, some selected publications on the use of RST in earthquake disaster reduction are shortly reviewed.  Then, various possibilities for improvement, which can help the development of RST for seismic disaster early warning are briefly explained, and finally, selection of the proper RST, by considering the existing techniques and equipment and also the natural, cultural, and economical conditions of developing countries is addressed.

a review on The Use of RSt in Seismic RISK Mitigation

The use of RST for seismic risk mitigation purposes goes back to early 70s. One of the first related techniques that can be mentioned is “Side-Looking Radar Imagery” (Kedar and Hsu, 1972).  In recent decade more attention has been paid to the use of RS for natural hazards mitigation, and it has been claimed that RS has a unique role in natural hazard assessment and mitigation (Wadge, 1994).  Airborne and satellite RSTs are among the newly developed ones for gathering damage information (Yamazaki et al., 1998; Matsuoka and Yamazaki, 2000).  In those studies, Yamazaki and his colleagues by using RS data obtained before and after the 1995 Hyogoken-Nanbu earthquake, have examined the accuracy of several RSTs from the viewpoint of detection for building damage.

A similar damage detection study has been performed on the 1999 Kocaeli, Turkey earthquake (Estrada et al., 2000) by using Landsat/TM images.  Another similar study has been done with regard to 2001 Gujarat, India earthquake (Yusuf et al., 2002).  The damage of 2001 Bhuj, India earthquake has been also studied in a multidisciplinary approach based on high resolution satellite imagery (Chiroiu et al., 2002).  Their study provides a fast loss estimation method in terms of physical damage and human casualties.  It has been claimed that the results could be very useful for the rescue teams deployed immediately after the catastrophe. Very recently in an MCEER publication a study has been reported entitled "Resilient Disaster Response: Using Remote Sensing Technologies for Post-Earthquake Damage Detection" (Eguchi et al., 2003).  Eguchi and his colleagues have studied the damages induced by the 1999 Marmara (Kocaeli), Turkey earthquake. They have claimed that their proposed techniques can be effectively employed to determine the extent of damages in urban buildings.  However, their results show that their techniques are basically useful for  heavily damaged buildings rather than moderately or slightly damaged ones.  This can be considered as a limitation in the use of their proposed techniques.

selection of the proper rst for developing countries

The advantages and limitations of the optical and Side Aperture Radar (SAR) sensing systems as the two main tools of RST have been given in Table 1.

Table 1. Comparison of optical and radar satellite imagery (After Eguchi et al., 2003)

| Sensor | Advantages | Limitations |
| --- | --- | --- |
| Optical | - Images are easy to understand & interpret - Imagery is comparable to human vision | - Obscured by cloud & smoke - Limited to daylight hours - Low revisit frequency |
| SAR | - Day and night imaging capability - Penetrates cloud & smoke - High revisit frequency | - Image interpretation is complicated, as SAR records backscatter - Subject to considerable noise - Sideways looking sensor causes layover issues |

It has been observed that these two systems can be very effective for damage detection if they are employed together, and their results are combined.  On the other hand, recent earthquakes in Turkey and India showed that the main cause of human casualty in developing countries due to earthquake is the collapsed buildings.  Therefore, it is quite reasonable for developing countries to plan for the combined use of optical and SAR systems for building collapse detection.  This will provide the emergency management authorities with the more reliable information on the casualties distribution, which is a key point in the success of disaster mitigation actions.

Conclusion

This study shows that using combination of optical and SAR systems for providing real time information on the extent of damages in different parts of stricken areas can be very effective in minimising the future earthquake losses.  Some improvements are necessary to make RST more effective for disaster early warning among which increasing the revisit frequency of optical system is the most desirable one.  Fortunately, the trend on RST development is promising in this regard.

REFERENCES

Chiroiu, L.; André, G.; Guillande, R.; 2 and Bahoken, F., 2002, "Earthquake Damage Assessment Using High Resolution Satellite Imagery", 7th U.S. National Conf. on Earthquake Eng., Earthquake Eng. Research Institute, Oakland, California.

Eguchi, R. T.; Huyck, C. K.; Adams, B. J.; Mansouri, B.; Houshmand, B.; and Shinozuka, M., 2003, "Resilient Disaster Response: Using Remote Sensing Technologies for Post-Earthquake Damage Detection", in MCEER Research Progress and Accomplishments, 2001-2003, State Univ. of New York at Buffalo, pages 125-137.

Estrada, Miguel; Matsuoka, Masashi; Yamazaki, Fumio, 2000, "Spectral Analysis of Optical Remote Sensing Images for the Detection of Damage due to the 1999 Kocaeli", Turkey earthquake, Seisan-Kenkyu, 52, 12, pages 586-589.

Kedar, E. Y.; Hsu, S.-Y., 1972, "Side-Looking Radar Imagery Applied in Seismic-Risk Mapping", Eighth International Symposium on Remote Sensing of the Environment, Willow Run Laboratories, University of Michigan, Ann Arbor, Oct. 2-6.

Matsuoka, Masashi; Yamazaki, Fumio, Mar. 2000, "Satellite Remote Sensing of Damaged Areas due to the 1995 Kobe Earthquake", Confronting Urban Earthquakes: Report of Fundamental Research on the Mitigation of Urban Disasters Caused by Near-Field Earthquakes, Kyoto University, Kyoto, Japan, pages 259-262.

Wadge, G. ed., 1994, "Natural Hazards and Remote Sensing", Natural Environment Research Council, London, 101 pages.

Yamazaki, Fumio; et al., Nov. 1998, "Airborne and Satellite Remote Sensing Technologies for Gathering Damage Information", EDM Technical Report Series No. 2, Multi-lateral Workshop on Development of Earthquake and Tsunami Disaster Mitigation Technologies and their Integration for the Asia-Pacific Region, Earthquake Disaster Mitigation Research Center, RIKEN, Miki, Japan, pages 167-180.

Yusuf, Y.; Matsuoka, M.; Yamazaki, F., 2002, "Detection of Building Damages due to the 2001 Gujarat, India Earthquake Using Satellite Remote Sensing", 7th U.S. National Conf. on Earthquake Eng., Earthquake Eng. Research Institute, Oakland, California.