The International Charter “Space and Major Disasters” and

examples of flood warning improvement with information from space.

Dr. Wolfgang Steinborn

DLR - Deutsches Zentrum für Luft- und Raumfahrt / German Aerospace Centre

Koenigswinterer Str. 522

D-53227 Bonn

50°43'5''N, 7°9'29''E, 65mH

E-Mail: wolfgang.steinborn@dlr.de

Fon: -49-(0)-228-447-599

Fax: -49-(0)-228-447-791

Extended Abstract

The motto “Think Globally – Act Locally” is often cited in the concern of preserving the Planet Earth and guaranteeing future generations’ life. Its implementation requires evidence of both, global and local character. This should preferably be seamless, to see things in the contextual overview and compare different regions under equal terms. Humanity has worked out such a method in the form of Earth observing satellites, and the paper will inform about progresses made since EWC-I, which included a whole session on “The role of Satellite Techniques in Early Warning”.

Two principal things have emerged since 1998: first, there was no “Charter” and second, there are now more and better satellites in orbit (the European Envisat with an innovative environmental instrumentation and the fleet of 3 sub-meter resolution satellites from USA, to mention but a few). What has not been achieved in the 5 years’ timeframe is a dedicated observation system with short reaction times for early warning and disaster management. This might explain, why the commitment of the EWC-I Final Declaration

“Public authorities and private organizations concerned with early warning and related practices should realize the benefits of partnership in the development of technological innovation and related commercial opportunities. This may include the expanded use of technologies related to earth observation, telecommunications, and other information technologies, including geographical information systems”.

has not become reality to large extent.

The “Charter”

On initiative of the United Nations space agencies from all over the world agreed in November 2000 to make available free-of-charge satellite images in the immediate suite of a major disaster. The International Charter (www.disasterscharter.org) aims at putting into operation past space investments by providing in short response time useful situation overviews to those affected by natural or man-made disasters, through authorized channels. A 24-hour on-duty operator prepares an archive and acquisition plan using available satellite resources (Fig.1).

The charter has been activated more than 40 times and has supported early warning and disaster relief operations with actual map information such as hazard extent, usable infrastructure and resources, destroyed buildings or pollution of water and land environment. The activation record is shown in the table:

| Type of Disaster | Location | Date of Activation |
| --- | --- | --- |
| Forest fires in British Columbia | Canada | August 07, 2003 |
| Flooding and Landslides in Nepal | Nepal | August 07, 2003 |
| Forest Fires in Portugal | Portugal | August 04, 2003 |
| Forest Fires in the Var Region | France | July 19, 2003 |
| Soufriere Hills Volcano Eruption in Montserrat | Montserrat | July 12, 2003 |
| Earthquake in Algeria | Algeria | May 22, 2003 |
| Earthquake in Turkey | Turkey | May 07, 2003 |
| Floods in Argentina | Argentina | April 30, 2003 |
| Hurricane in India | India | April 24, 2003 |
| Stromboli Volcano Eruption | Italy | April 09, 2003 |
| Floods in Morocco | Morocco | November 28, 2002 |
| Oil Spill off the Coast of Galicia | Spain | November 14, 2002 |
| Oil Spill in the Gulf of Aden | Gulf of Aden | October 6, 2002 |
| Hurricane in Yukatan | Mexico | October 4, 2002 |
| Landslide in North Ossetia | Russia | September 27, 2002 |
| Flooding in south-eastern France | France | September 9, 2002 |
| Flooding of the Elbe River | Germany | August 22, 2002 |
| Flooding of the Danube River | Austria | August 20, 2002 |
| Flooding in Znojmo (South Moravia) | Czech Republic | August 17, 2002 |
| Flooding in Caucasia | Russia | June 28, 2002 |
| Flooding in British Columbia | Canada | June 18, 2002 |
| Flooding in Manitoba | Canada | June 13, 2002 |
| Landslides in Lago Maggiore | Italy | May 26, 2002 |
| Earthquakes | Afghanistan | March 28, 2002 |
| Mount Nyiragongo Volcano Eruption | Congo (DRC) | January 21, 2002 |
| Flooding in the NE of France | France | December 31, 2001 |
| Nias Island Flooding and Landslides | Indonesia | August 1, 2001 |
| Mount Etna Volcano Eruptions | Italy | July 26, 2001 |
| Lena River Flooding | Siberia | May 22, 2001 |
| Oil Spill | Denmark | March 30, 2001 |
| Oil Spill | Lebanon | March 30, 2001 |
| Saône River Flooding | France | March 22, 2001 |
| Earthquake | El Salvador | February 14, 2001 |
| Earthquake | India | January 29, 2001 |
| Oil Spill, Marine Pollution | Galapagos | January 26, 2001 |
| Earthquake and Landslide | El Salvador | January 15, 2001 |
| Landslide | Slovenia | November 11, 2000 |

Based on this offer numerous services emerged in recent years which try to improve forecast modelling or risk mapping for various kinds of disasters. Fig.2 shows a map of different flood extents derived from satellite images released under the charter from which a de-warning could be issued for downstream areas.

Flood forecast model improvement

Significant improvements of operational flood warning services can be obtained with satellite images available on a daily basis (Fig.3). This is the result of a German project that responds to International River Commissions’ call to prolong warning lead times from 12 hours 1998 to 24 hours by 2005 and up to 48 hours in the future. It integrates satellite-derived land surface parameters (water saturation of soils, snow

cover) with weather forecasts and in-situ measurements into a runoff simu-lation model for the whole river catch-ment (Mosel, 28000 km², in this case).

In close exchange with other projects for the same river in neighbour countries (France, Luxembourg), focussing on complementary aspects (risk zone delineation and high-resolution restriction compliance monitoring of construction in endangered areas; improving the warning chain with communication satellites) and favourably involving all political and technical levels, the basis was laid for a subsequent project, encouraged by the regional prime ministers, for a model flood management information-system for cross-boundary river basins.

Conclusions:

- Satellite observation (as before satellite navigation and communication) has become mature enough to be a building block of warning chains in all countries and on all political levels

- Provisions must be taken now to fill the information gaps after expiry of the lifetime of the present satellite generation (GMES = European part?).

- Effective disaster warning and relief requires an own dedicated observation system (such as past global satellite fleets for weather forecast, navigation and military intelligence) with high resolution and fast reaction capability; investment costs are much lower than economic losses without the information

- Access for all countries must be organised similar to the present Charter (information extraction will become cheap through automation); field forces must be equipped with mobile data handling units

- Work must be applied to a worldwide assimilation of standards for maps of risks and rescue potential as well as continued monitoring of construction and other changes in endangered areas ensured

# Text boxes

Fig.3:	Unprecedented floods hit the town of Santa Fe/Argentina in 2003. The Charter was triggered by the Argentinean Federal Emergency System on 30.4., and 2 satellite images of 1.4. and 3.4.2003 evaluated to map different flood stages (grey levels), leading to a counter-warning for downstream areas

Fig.1: 	Satellite data can be obtained from the 5 space agencies listed top right in the case that an “authorized user”, normally a high level civil protection officer or a crisis centre accredited to the charter, calls the On-Duty-Operator. In most cases the space agencies’ commitment includes also interpretation of the data within a contract with a value added reseller

Fig.3:	Scheme of the incorporation of satellite-derived surface data into an operational flood forecast model (Large Area Runoff Simulation= LARSIM). They provide the geographic coverage that in situ mea-surements never can render; thus they interpolate other data. The map shows the true snow extend from a satellite image (Left) compared with the one modelled from weather data for the 14000 km² catchment of the Neckar river.